## Slide 1: Logisim
Open-source (i.e. free!) “graphical tool for designing and simulating logic circuits”
  Runs on Java on any computer
  Download to your home computer via class login or the Logisim website (we are using version 2.7.1)
No programming involved
  Unlike Verilog, which is a hardware description language (HDL)
  Click and drag; still has its share of annoying quirks
http://ozark.hendrix.edu/~burch/logisim/

## Slide 2: Gates in Logisim
Click gate type, click to place
  Can set options before placing or select gate later to change
Options
Types of Gates
bus width n
# inputs
labeling not necessary, but can help

## Slide 3: Registers in Logisim
Flip-flops and Registers in “Memory” folder
8-bit accumulator:

## Slide 4: Wires in Logisim
Click and drag on existing port or wire
Color schemes:
  Gray: unconnected
  Dark Green: low signal (0)
  Light Green: high signal (1)
  Red: error
  Blue: undetermined signal
  Orange: incompatible widths
Tunnels: all tunnels with same label are connected
“Splitter” used to adjust bus widths

## Slide 5: Common Mistakes in Logisim
Connecting wires together
  Crossing wires vs. connected wires
Losing track of which input is which
  Mis-wiring a block (e.g. CLK to Enable)
  Grabbing wrong wires off of splitter
Errors:

## Slide 6: Agenda
State Elements Continued
Administrivia
Logisim Introduction
Finite State Machines
Multiplexers
ALU Design
  Adder/Subtracter

## Slide 7: Finite State Machines (FSMs)
You may have seen FSMs in other classes
Function can be represented with a state transition diagram
With combinational logic and registers, any FSM can be implemented in hardware!
. . .

## Slide 8: FSM Overview
An FSM (in this class) is defined by:
  A set of states S (circles)
  An initial state s0 (only arrow not between states)
  A transition function that maps from the current input and current state to the output and the next state (arrows between states)
State transitions are controlled by the clock:
  On each clock cycle the machine checks the inputs and generates a new state (could be same) and new output

## Slide 9: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
States: S0, S1, S2
Initial State: S0
Transitions of form:
input/output

## Slide 10: Hardware Implementation of FSM
Register holds a representation of the FSM’s state
  Must assign a unique bit pattern for each state
  Output is present/current state (PS/CS)
  Input is next state (NS)
Combinational Logic implements transition function (state transitions + output)
+
=

## Slide 11: FSM: Combinational Logic
Read off transitions into Truth Table!
  Inputs: Current State (CS) and Input (In)
  Outputs: Next State (NS) and Output (Out)
Implement logic for EACH output (2 for NS, 1 for Out)
CS | In | NS | Out
00 | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 0 | 00 | 0
01 | 1 | 10 | 0
10 | 0 | 00 | 0
10 | 1 | 00 | 1
Notes: In lecture: Implement logic for Out (1 NOT, 2 AND gates)

## Slide 12: Unspecified Output Values (1/2)
Our FSM has only 3 states
  2 entries in truth table are undefined/unspecified
Use symbol ‘X’ to mean it can be either a 0 or 1
  Make choice to simplify final expression
CS | In | NS | Out
00 | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 0 | 00 | 0
01 | 1 | 10 | 0
10 | 0 | 00 | 0
10 | 1 | 00 | 1
11 | 0 | XX | X
11 | 1 | XX | X

## Slide 13: Unspecified Output Values (2/2)
Let’s find expression for NS1
  Recall: 2-bit output is just a 2-bit bus, which is just 2 wires
Boolean algebra:
  NS1 = CS1’CS0In + CS1CS0In’ + CS1CS0In
  NS1 = CS0In
Karnaugh Map:
  NS1 = CS0In
CS | In | NS | Out
00 | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 0 | 00 | 0
01 | 1 | 10 | 0
10 | 0 | 00 | 0
10 | 1 | 00 | 1
11 | 0 | XX | X
11 | 1 | XX | X
Differs by 2
Is neighbor
 | 00 | 01 | 11 | 10
0 | 0 | 0 | X | 0
1 | 0 | 1 | X | 0
CS
In

## Slide 14: 3 Ones FSM in Hardware
  2-bit Register needed for state
  CL: NS1 = CS0In, NS0 = CS1’CS0’In, Out = CS1In

## Slide 15: Agenda
State Elements Continued
Administrivia
Logisim Introduction
Finite State Machines
Multiplexers
ALU Design
  Adder/Subtracter

## Slide 16: Data Multiplexor
Multiplexor (“MUX”) is a selector
  Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value

## Slide 17: Implementing a 1-bit 2-to-1 MUX
Schematic:
Truth Table:
Boolean Algebra:
Circuit Diagram:
s | a | b | c
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 18: 1-bit 4-to-1 MUX (1/2)
Schematic:
Truth Table: How many rows?
Boolean Expression: e = s1’s0’a + s1’s0b + s1s0’c + s1s0d

## Slide 19: 1-bit 4-to-1 MUX (2/2)
Can we leverage what we’ve previously built?
  Alternative hierarchical approach:

## Slide 20: Subcircuits Example
Logisim equivalent of procedure or method
  Every project is a hierarchy of subcircuits
Incomplete wiring shown here