## Slide 1
计算机组成
MIPS控制
高小鹏
北京航空航天大学计算机学院
系统结构研究所
计算机学院课程

## Slide 2: 提纲
内容主要取材
  CS617的21讲
快速回顾数据通路
实现控制
时钟方法

## Slide 3: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We are here

## Slide 4: Hardware Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks
Today

## Slide 5: 提纲
内容主要取材
  CS617的21讲
快速回顾数据通路
实现控制
时钟方法

## Slide 6: Datapath Review
Part of the processor; the hardware necessary to perform all operations required
  Depends on exact ISA, RTL of instructions
Major components:
  PC and Register File (RegFile holds registers)
  Instruction and Data Memory
  ALU for operations (on two operands)
  Extender (sign/zero extend)

## Slide 7: Five Stages of the Datapath
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
1. Instruction
Fetch

## Slide 8: Datapath and Control
Route parts of datapath based on ISA needs
  Add MUXes to select from multiple inputs
  Add control signals for component inputs and MUXes
Analyze control signals
  How wide does each one need to be?
  For each instruction, assign appropriate value for correct routing

## Slide 9: MIPS-lite Instruction Fetch
imm16
CLK
PC
4
PC Ext
Adder
Adder
MUX
0
1
32
Instruction
Addr
Instruction
Memory
Instr Fetch Unit
nPC_sel
zero

## Slide 10: MIPS-lite Datapath Control Signals
ExtOp: 0  “zero”; 1  “sign”
ALUsrc: 0  busB; 1  imm16
ALUctr: “ADD”, “SUB”, “OR”
nPC_sel: 0  +4; 1  branch
MemWr: 1  write memory
MemtoReg: 0  ALU; 1  Mem
RegDst: 0  “rt”; 1  “rd”
RegWr: 1  write register
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
nPC_sel
Instr
Fetch
Unit
CLK

## Slide 11: 提纲
内容主要取材
  CS617的21讲
快速回顾数据通路
实现控制
时钟方法

## Slide 12: Processor Design Process
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output
Now

## Slide 13: Purpose of Control
Controller
ALUctr
RegDst
ALUSrc
ExtOp
MemtoReg
MemWr
nPC_sel
Datapath
RegWr
Instruction<31:0>
<20:16>
<15:11>
<5:0>
<0:15>
imm16
rd
rs
rt
Instr
Memory
opcode
<25:21>
funct
<31:26>

## Slide 14: MIPS-lite Instruction RTL
Instr Register Transfer Language
addu R[rd]R[rs]+R[rt]; PCPC+4
subu R[rd]R[rs]–R[rt]; PCPC+4
ori R[rt]R[rs]+zero_ext(imm16); PCPC+4
lw R[rt]MEM[R[rs]+sign_ext(imm16)]; PCPC+4
sw MEM[R[rs]+sign_ext(imm16)]R[rs]; PCPC+4
beq if(R[rs]==R[rt]) then PCPC+4+[sign_ext(imm16)||00] else PCPC+4

## Slide 15: MIPS-lite Control Signals (1/2)
Instr Control Signals
addu ALUsrc=RegB, ALUctr=“ADD”, RegDst=rd, RegWr, nPC_sel=“+4”
subu ALUsrc=RegB, ALUctr=“SUB”, RegDst=rd, RegWr, nPC_sel=“+4”
ori ALUsrc=Imm, ALUctr=“OR”, RegDst=rt, RegWr, ExtOp=“Zero”, nPC_sel=“+4”
lw ALUsrc=Imm, ALUctr=“ADD”, RegDst=rt, RegWr, ExtOp=“Sign”, MemtoReg, nPC_sel=“+4”
sw ALUsrc=Imm, ALUctr=“ADD”, MemWr, ExtOp=“Sign”, nPC_sel=“+4”
beq ALUsrc=RegB, ALUctr=“SUB”, nPC_sel=“Br”

## Slide 16: MIPS-lite Control Signals (2/2)
add
sub
ori
lw
sw
beq
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPC_sel
ExtOp
ALUctr<2:0>
1
0
0
1
0
0
X
Add
1
0
0
1
0
0
X
Subtract
0
1
0
1
0
0
0
Or
0
1
1
1
0
0
1
Add
X
1
X
0
1
0
1
Add
X
0
X
0
0
1
X
Subtract
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
Green Sheet
10 0000
See MIPS
10 0010
n/a
Control Signals
All Supported Instructions
Now how do we implement this table with CL?

## Slide 17: Generating Boolean Expressions
Idea #1: Treat instruction names as Boolean variables!
  opcode and funct bits are available to us
  Use gates to generate signals that are 1 when it is a particular instruction and 0 otherwise
Examples:
  beq = op[5]’∙op[4]’∙op[3]’∙op[2]∙op[1]’∙op[0]’
  Rtype = op[5]’∙op[4]’∙op[3]’∙op[2]’∙op[1]’∙op[0]’
  add = Rtype∙funct[5]∙funct[4]’∙funct[3]’ ∙funct[2]’∙funct[1]’∙funct[0]’

## Slide 18: Generating Boolean Expressions
Idea #2: Use instruction variables to generate control signals
  Make each control signal the combination of all instructions that need that signal to be a 1
Examples:
  MemWrite = sw
  RegWrite = add + sub + ori + lw
What about don’t cares (X’s)?
  Want simpler expressions; set to 0!
Read from row of table

## Slide 19: Controller Implementation
“AND” Logic
add
sub
ori
lw
sw
beq
“OR” Logic
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPC_sel
ExtOp
ALUctr[0]
ALUctr[1]
opcode
funct
Use these two ideas to design controller:
Generate instruction signals
Generate control signals

## Slide 20: AND Control Logic in Logisim
Notes: Logisim file called “Control Plane MIPS.circ”

## Slide 21: OR Control Logic in Logisim

## Slide 22: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
CALL HOME, WE’VE MADE HARDWARE/SOFTWARE CONTACT!!!

## Slide 23: 提纲
内容主要取材
  CS617的21讲
快速回顾数据通路
实现控制
时钟方法

## Slide 24: Register Timing Terms (Review)
Setup Time: how long the input must be stable before the CLK trigger for proper input read
Hold Time: how long the input must be stable after the CLK trigger for proper input read
“CLK-to-Q” Delay: how long it takes the output to change, measured from the CLK trigger

## Slide 25: Maximum Clock Frequency
What is the max frequency of this circuit?
  Limited by how much time needed to get correct Next State to Register
Max Delay =
Max Freq = 1/Max Delay
Setup Time
+ CLK-to-Q Delay
+ CL Delay
Notes: Hold time is included in CLK-to-Q delay.

## Slide 26: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register
1
2
3
4
Critical Path =
CL Delay 1
+ CL Delay 2
+ CL Delay 3
+ Adder Delay

## Slide 27: Clocking Methodology
Storage elements (RegFile, Mem, PC) triggered by same clock
Critical path determines length of clock period
  This includes CLK-to-Q delay and setup delay
So far we have built a single cycle CPU – entire instructions are executed in 1 clock cycle
  Up next: pipelining to execute instructions in 5 clock cycles
Clk
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 28: Register-Register Timing: One Complete Cycle for addu
Clk
PC
Rs, Rt, Rd,
Op, Func
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
Rd
Clk-to-Q
Setup Time
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time.
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this later.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)

## Slide 29: Register-Register Timing: One Complete Cycle for addu
Clk
PC
Rs, Rt, Rd,
Op, Func
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
Rd
Clk-to-Q
Setup Time
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time.
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this later.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)

## Slide 30: Single Cycle Performance
Assume time for actions are 100ps for register read or write; 200ps for other events
Minimum clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
What can we do to improve clock rate?
Will this improve performance as well?
  Want increased clock rate to mean faster programs
Notes: 1.25 GHz

## Slide 31: 作业1
《计算机组成与设计》 | Logicsim | WORD
4.3 |  | 
4.4 |  | 
4.5 | (4.5.1) | 
4.7 |  | 
4.10 |  | 

## Slide 32: Project3
示意图

## Slide 33: Project3
Logicsim
  设计1、以作业2为基础，实现PPT中MIPS-lite指令集的单周期数据通路
  设计2、以设计1为基础，实现MIPS-lite指令集的单周期数据通路
  设计1、设计2应分别是2个独立的设计图
    不要直接在设计1的设计图上增加设计2的部分！

## Slide 34: Project3
Logicsim
  以上次作用3的设计2为基础，实现完整的单周期CPU
  构造一个至少20条以上指令的测试程序
    每个类型的指令必须出现1次以上
Word
  简要论述设计要点，并对测试用例及测试结果进行简单分析

## Slide 36: MIPS-lite控制信号
 | ADDU | SUBU | ORI | LW | SW | BEQ
nPC_sel | “+4” |  |  |  |  | 
RegDst | rd |  |  |  |  | 
ALUSrc | RegB |  |  |  |  | 
ALUctl | “ADD” |  |  |  |  | 
ExtOp |  |  |  |  |  | 
MemtoReg |  |  |  |  |  | 
RegWr | 1 |  |  |  |  | 
MemWr |  |  |  |  |  | 
nPC_sel
ADDU
SUBU
ORI
LW

## Slide 37: MIPS-lite控制信号
 | ADDU | SUBU | ORI | LW | SW | BEQ
nPC_sel | “+4” |  |  |  |  | 
RegDst | rd |  |  |  |  | 
ALUSrc | RegB |  |  |  |  | 
ALUctl | “ADD” |  |  |  |  | 
ExtOp |  |  |  |  |  | 
MemtoReg |  |  |  |  |  | 
RegWr | 1 |  |  |  |  | 
MemWr |  |  |  |  |  | 

## Slide 38: MIPS-lite Control Signals (1/2)
Instr Control Signals
addu ALUsrc=RegB, ALUctr=“ADD”, RegDst=rd, RegWr, nPC_sel=“+4”
subu ALUsrc=RegB, ALUctr=“SUB”, RegDst=rd, RegWr, nPC_sel=“+4”
ori ALUsrc=Imm, ALUctr=“OR”, RegDst=rt, RegWr, ExtOp=“Zero”, nPC_sel=“+4”
lw ALUsrc=Imm, ALUctr=“ADD”, RegDst=rt, RegWr, ExtOp=“Sign”, MemtoReg, nPC_sel=“+4”
sw ALUsrc=Imm, ALUctr=“ADD”, MemWr, ExtOp=“Sign”, nPC_sel=“+4”
beq ALUsrc=RegB, ALUctr=“SUB”, nPC_sel=“Br”